## Slide 1: Network Transport Layer: TCP
This deck of slides are heavily based on CPSC 433/533 at Yale University, by courtesy of Dr. Y. Richard Yang.
  Qiao Xiang, Congming Gao, Qiang Su
  https://sngroup.org.cn/courses/cnns-xmuf25/index.shtml
  11/04/2025

## Slide 2: Outline
Admin and recap
TCP

## Slide 3: rdt3.0: Stop-and-Wait Performance
first packet bit transmitted, t = 0
sender
receiver
RTT
last packet bit transmitted, t = L / R
first packet bit arrives
last packet bit arrives, send ACK
ACK arrives, send next
packet, t = RTT + L / R
  What is Usender: utilization – fraction of time link busy sending?
Assume: 1 Gbps link, 15 ms e-e prop. delay, 1KB packet
3

## Slide 4
Recap: Reliable Transport
Basic structure: sliding window protocols
Realization: GBN or SR
General technique: pipelining.

## Slide 5: TCP Reliable Data Transfer
Connection-oriented:
  connection management
    setup (exchange of control msgs) init’s sender, receiver state before data exchange
    close
Full duplex data:
  bi-directional data flow in same connection
A sliding window protocol
  a combination of go-back-n and selective repeat:
    send & receive buffers
    cumulative acks
    TCP uses a single retransmission timer
    do not retransmit all packets upon timeout

## Slide 6: Flow Control
receive side of a connection has a receive buffer:
speed-matching service: matching the send rate to the receiving app’s drain rate
app process may be slow at reading from buffer
sender won’t overflow
receiver’s buffer by
transmitting too much,
too fast
flow control

## Slide 7: TCP Flow Control: How it Works
spare room in buffer
= RcvWindow
source port #
dest port #
application
data
(variable length)
sequence number
acknowledgement number
rcvr window size
ptr urgent data
checksum
F
S
R
P
A
U
head
len
not
used
Options (variable length)

## Slide 8
TCP Seq. #’s and ACKs
Seq. #’s:
  byte stream “number” of first byte in segment’s data
ACKs:
  seq # of next byte expected from other side
  cumulative ACK in standard header
  selective ACK in options
Host A
Host B
Seq=42, ACK=79, data = ‘C’
Seq=79, ACK=43, data = ‘C’
Seq=43, ACK=80
User
types
‘C’
host ACKs
receipt
of echoed
‘C’
host ACKs
receipt of
‘C’, echoes
back ‘C’
time
simple telnet scenario

## Slide 9: TCP Send/Ack Optimizations
TCP includes many tune/optimizations, e.g.,
  the “small-packet problem”: sender sends a lot of small packets (e.g., telnet one char at a time)
    Nagle’s algorithm: do not send data if there is small amount of data in send buffer and there is an unack’d segment
  the ”ack inefficiency” problem: receiver sends too many ACKs, no chance of combing ACK with data
    Delayed ack to reduce # of ACKs/combine ACK with reply

## Slide 10: TCP Receiver ACK Generation [RFC 1122, RFC 2581]
Event at Receiver
Arrival of in-order segment with
expected seq #. All data up to
expected seq # already ACKed
Arrival of in-order segment with
expected seq #. One other
segment has ACK pending
Arrival of out-of-order segment
higher-than-expect seq. # .
Gap detected
Arrival of segment that
partially or completely fills gap
TCP Receiver Action
Delayed ACK. Wait up to 500ms
for next segment. If no next segment,
send ACK
Immediately send single cumulative
ACK, ACKing both in-order segments
Immediately send duplicate ACK,
indicating seq. # of next expected byte
Immediate send ACK, provided that
segment starts at lower end of gap

## Slide 11
Outline
Admin and Recap
Reliable data transfer
  perfect channel
  channel with bit errors
  channel with bit errors and losses
  sliding window: reliability with throughput
TCP reliability
  data seq#, ack, buffering
  timeout realization

## Slide 12
TCP Reliable Data Transfer
Basic structure: sliding window protocol
Remaining issue: How to determine the “right” parameters?
  timeout value?
  sliding window size?

## Slide 13
History
Key parameters for TCP in mid-1980s
  fixed window size W
  timeout value = 2 RTT
Network collapse in the mid-1980s
  UCB  LBL throughput dropped by 1000X !
The intuition was that the collapse was caused by wrong parameters…

## Slide 14: Timeout: Cost of Timeout Param
Why is good timeout value important?
too short
  premature timeout
  unnecessary retransmissions; many duplicates
too long
  slow reaction to segment loss
Q: Is it possible to set Timeout as a constant?
Q: Any problem w/ the early approach: Timeout = 2 RTT

## Slide 15: Setting Timeout
Problem:
Ideally, we set timeout = RTT, but RTT is not a fixed value => using the average of RTT will generate many timeouts due to network variations
Possibility: using the average/median of RTT
Issue: this will generate many timeouts due to network variations
Solution:
Set Timeout RTO = avg + “safety margin” based on variation
Timeout = EstRTT + 4 * DevRTT
TCP approach:
RTT
freq.

## Slide 16: Compute EstRTT and DevRTT
EstRTT = (1-alpha)*EstRTT + alpha*SampleRTT
Exponential weighted moving average (EWMA)
  influence of past sample decreases exponentially fast
- SampleRTT: measured time from segment transmission until ACK receipt
- typical value: alpha = 0.125
DevRTT = (1-beta)*DevRTT + beta|SampleRTT-EstRTT|
(typically, beta = 0.25)

## Slide 17: An Example TCP Session

## Slide 18: Fast Retransmit
Issue: Timeout period often relatively long:
  long delay before resending lost packet
Question: Can we detect loss faster than RTT?
If sender receives 3 ACKs for the same data, it supposes that segment after ACKed data was lost:
  resend segment before timer expires
Detect lost segments via duplicate ACKs
  sender often sends many segments back-to-back
  if segment is lost, there will likely be many duplicate ACKs

## Slide 19
Triple Duplicate Ack
1
2
3
4
5
6
Packets
Acknowledgements (waiting seq#)
7
2
3
4
4
4
4

## Slide 20: Fast Retransmit:
event: ACK received, with ACK field value of y
if (y > SendBase) {
…
SendBase = y
if (there are currently not-yet-acknowledged segments)
start timer
…
}
else {
increment count of dup ACKs received for y
if (count of dup ACKs received for y = 3) {
resend segment with sequence number y
…
a duplicate ACK for
already ACKed segment
fast retransmit

## Slide 21: TCP: reliable data transfer
00 sendbase = initial_sequence number agreed by TWH
01 nextseqnum = initial_sequence number by TWH
02 loop (forever) {
03 switch(event)
04 event: data received from application above
05 if (window allows send)
06 create TCP segment with sequence number nextseqnum
06 if (no timer) start timer
07 pass segment to IP
08 nextseqnum = nextseqnum + length(data) else put packet in buffer
09 event: timer timeout for sendbase
10 retransmit segment
11 compute new timeout interval
12 restart timer
13 event: ACK received, with ACK field value of y
14 if (y > sendbase) { /* cumulative ACK of all data up to y */
15 cancel the timer for sendbase
sendbase = y
if (no timer and packet pending) start timer for new sendbase
while (there are segments and window allow)
sent a segment;
18 }
19 else { /* y==sendbase, duplicate ACK for already ACKed segment */
20 increment number of duplicate ACKs received for y
21 if (number of duplicate ACKS received for y == 3) {
22 /* TCP fast retransmit */
23 resend segment with sequence number y
24 restart timer for segment y
25 }
26 } /* end of loop forever */
Simplified
TCP
sender

## Slide 22
Outline
Admin and Recap
Reliable data transfer
  perfect channel
  channel with bit errors
  channel with bit errors and losses
  sliding window: reliability with throughput
TCP reliability
  data seq#, ack, buffering
  timeout realization
  connection management

## Slide 23: Why Connection Setup/When to Accept (Safely Deliver) First Packet?
sender
receiver
ACK for 0
accept
data 0

## Slide 24: Why Connection Setup/When to Accept (Safely Deliver) First Packet?
sender
receiver
ACK for 0 (n)
accept
data 0 (transfer $1000 to B)
data 0 (transfer $1000 to B)
accept?
24
Notes: a sender should not reuse a seq# before it is sure the packet has left the network

## Slide 25: Transport “Safe-Setup” Principle
A general safety principle for a receiver R to accept a message from a sender S is the general “authentication” principle, which consists of two conditions:
  Transport authentication principle:
  [p1] Receiver can be sure that what Sender says is fresh
  [p2] Receiver receives something that only Sender can say
We first assume a secure setting: no malicious attacks.
Exercise: Techniques to allow a receiver to check for freshness (e.g., add a time stamp)?

## Slide 26: Generic Challenge-Response Structure Checking Freshness
sender
receiver
Challenge (nonce)
deliver
I have data to send
Demonstrate knowing nonce; data

## Slide 27: Three Way Handshake (TWH) [Tomlinson 1975]
Host A
SYN(seq=x)
Host B
ACK(seq=x), SYN(seq=y)
ACK(seq=y)
DATA(seq=x+1)
SYN: indicates connection setup
accept data only after
verified y is bounced back
x is the init. seq
notify initial seq#. Accept?
think of y as a challenge
Notes: Syn(seq=x) could be duplicate or malicious

## Slide 28: Scenarios with Duplicate Request/SYN Attack
Host A
Host B
ACK(seq=x), SYN(seq=y)
REJECT(seq=y)
SYN(seq=x)
accept?
no such request
reject

## Slide 29: Scenarios with Duplicate Request/SYN Attack
Host A
Host B
ACK(seq=x), SYN(seq=y)
REJECT(seq=y)
SYN(seq=x)
accept?
no such request
reject
ACK(seq=z)

## Slide 30: Make “Challenge y” Robust
To avoid that “SYNC ACK y” comes from reordering and duplication
  for each connection (sender-receiver pair), ensuring that two identically numbered packets are never outstanding at the same time
    network bounds the life time of each packet
    a sender will not reuse a seq# before it is sure that all packets with the seq# are purged from the network
    seq. number space should be large enough to not limit transmission rate
Increasingly move to cryptographic challenge and response
Notes: Add QUIC design: QUIC uses a cryptographic handshake
  Servers
    front-end servers, which collectively handle billions of requests a day from web browsers and mobile apps across a wide range of services.
  On the client side, we have deployed QUIC in
    Chrome,
    our mobile video streaming YouTube app, and in the
    Google Search app on Android
TCP connections commonly incur at least one round-trip delay of connection setup time before any application data can be sent, and TLS adds two round trips to this delay

## Slide 31: Connection Close
Why connection close?
  so that each side can release resource and remove state about the connection (do not want dangling socket)
client
server
I am done. Are you done too?
I am done too. Goodbye!
init. close
close
close
release
resource?
release
resource?
release
resource?

## Slide 32: General Case: The Two-Army Problem
The gray (blue) armies need to agree on whether or not they will attack the white army. They achieve agreement by sending messengers to the other side. If they both agree, attack; otherwise, no. Note that a messenger can be captured!

## Slide 33: Time_Wait
Generic technique: Timeout to “solve” infeasible problem
  Instead of message-driven state transition, use a timeout based transition; use timeout to handle error cases
client
server
I am done. Are you done too?
I am done too. Goodbye!
init. close
close
close
release
resource?
release
resource?
release
resource?
Closed
Working
Time_Waiit
Working
Closed

## Slide 34: Time_Wait Design Options
Time to retransmit ACK
Host A
FIN
Host B
ACK
close
Design 2 (receiver time wait)
Close after first ACK
All states removed
All states removed
Host A
FIN
Host B
ACK
close
Time = n x timeout
Time to retry FIN after each timeout
Design 1 (initiator time wait)
Close after receive FIN
All states removed
All states removed

## Slide 35
%netstat -t -a
CLOSED
LISTEN
SYN RCVD
SYN
SYN/ACK
ACK
CLOSED
SYN SENT
ESTABLSIHED
ESTABLSIHED
FIN
ACK
ACK
FIN WAIT 1
ESTABLSIHED
ESTABLSIHED
CLOSE WAIT
FIN
LAST ACK
FIN WAIT 2
TIME WAIT

## Slide 36: TCP Connection Management
TCP lifecycle: init SYN/FIN
CLOSED
SYN RCVD
SYN
SYN/ACK
ACK
CLOSED
SYN SENT
ESTABLSIHED
FIN
ACK
ACK
FIN WAIT 1
ESTABLSIHED
ESTABLSIHED
CLOSE WAIT
FIN
LAST ACK
FIN WAIT 2
TIME WAIT
http://dsd.lbl.gov/TCP-tuning/ip-sysctl-2.6.txt

## Slide 37: TCP Connection Management
TCP lifecycle: wait for SYN/FIN
CLOSED
SYN RCVD
SYN
SYN/ACK
ACK
CLOSED
SYN SENT
ESTABLSIHED
FIN
ACK
ACK
FIN WAIT 1
ESTABLSIHED
ESTABLSIHED
CLOSE WAIT
FIN
LAST ACK
FIN WAIT 2
TIME WAIT

## Slide 38
A Summary of Questions
Basic structure: sliding window protocols
How to determine the “right” parameters?
  timeout: mean + variation
  sliding window size?

## Slide 39
Sliding Window Size Function: Rate Control
Transmission rate determined by congestion window size, cwnd, over segments:
cwnd segments, each with MSS bytes sent in one RTT:
Rate =
cwnd * MSS
RTT
Bytes/sec
cwnd
Assume W is small enough. Ignore small details. MSS: Minimum Segment Size

## Slide 40
Some General Questions
Big picture question:
How to determine a flow’s sending rate?
For better understanding, we need to look at a few basic questions:
What is congestion (cost of congestion)?
Why are desired properties of congestion control?

## Slide 41
Roadmap
What is congestion
The basic CC alg
TCP/reno CC
TCP/Vegas
A unifying view of TCP/Reno and TCP/Vegas
Network wide resource allocation
  Framework
  Axiom derivation of network-wide objective function
  Derive distributed algorithm

## Slide 42
Outline
Admin and recap
TCP Reliability
Transport congestion control
  what is congestion (cost of congestion)

## Slide 43
flow 2 (5 Mbps)
flow 1
router 1
router 2
10 Mbps
5 Mbps
20 Mbps
Cause/Cost of Congestion: Single Bottleneck
- Flow 2 has a fixed sending rate of 5 Mbps
- We vary the sending rate of flow 1 from 0 to 20 Mbps
- Assume
  no retransmission; link from router 1 to router 2 has infinite buffer
20 Mbps
20 Mbps
throughput: e2e packets delivered in unit time
Delay?
sending rate by flow 1 (Mbps)
throughput of flow 1 & 2 (Mbps)
5
10
5
0
sending rate by flow 1 (Mbps)
delay at central link
5
0
delay due to
randomness

## Slide 44
flow 2 (5 Mbps)
flow 1
router 1
10 Mbps
5 Mbps
20 Mbps
Cause/Cost of Congestion: Single Bottleneck
Assume
  no retransmission
  the link from router 1 to router 2 has finite buffer
  throughput: e2e packets delivered in unit time
20 Mbps
20 Mbps
Zombie packet: a packet dropped at the link from router 2 to router 5; the upstream transmission from router 1 to router 2 used for that packet was wasted!
router 3
router 4
router 2
router 5
router 6
sending rate by flow 1 (Mbps)
throughput of flow 1 & 2 (Mbps)
5
10
5
0
x

## Slide 45
Summary: The Cost of Congestion
When sources sending rate too high for the network to handle”:
Packet loss =>
  wasted upstream bandwidth when a pkt is discarded at downstream
  wasted bandwidth due to retransmission (a pkt goes through a link multiple times)
High delay
Load
Load
Delay
Throughput
knee
cliff
congestion
collapse
packet
loss