## Slide 1: Network Transport Layer: Network Resource Allocation Framework
  Qiao Xiang, Congming Gao, Qiang Su
  https://sngroup.org.cn/courses/cnns-xmuf25/index.shtml
11/11/2025
This deck of slides are heavily based on CPSC 433/533 at Yale University, by courtesy of Dr. Y. Richard Yang.

## Slide 2
Outline
Admin and recap
Transport congestion control
  what is congestion (cost of congestion)
  basic congestion control alg.
  TCP/Reno congestion control
  TCP Cubic
  TCP/Vegas
  network wide resource allocation
    general framework
    objective function: axiom derivation of network-wide objective function
    algorithm: general distributed algorithm framework
    application: TCP/Reno TCP/Vegas revisited
2

## Slide 3
x0
efficiency
efficiency: distributed linear rule
x0
intersection
x0
congestion
fairness
x0
b=1
a=0
b=1
a=0

## Slide 4
efficiency: distributed linear rule
x0
no-congestion
x0
efficiency
fairness
x0
convergence
x0

## Slide 5
TCP/Reno Full Alg
Initially:
cwnd = 1;
ssthresh = infinite (e.g., 64K);
For each newly ACKed segment:
if (cwnd < ssthresh) // slow start: MI
cwnd = cwnd + 1;
else
// congestion avoidance; AI cwnd += 1/cwnd;
Triple-duplicate ACKs:
// MD
cwnd = ssthresh = cwnd/2;
Timeout:
ssthresh = cwnd/2; // reset
cwnd = 1;
(if already timed out, double timeout value; this is called exponential backoff)

## Slide 6
TCP/Reno: Big Picture
Time
cwnd
slow
start (MI)
congestion
avoidance (AIMD)
TD
TD: Triple duplicate acknowledgements
TO: Timeout
TO
ssthresh
ssthresh
ssthresh
ssthresh
congestion
avoidance
TD
congestion
avoidance
slow
start
congestion
avoidance
TD

## Slide 7
Outline
Admin and recap
Transport congestion control
  what is congestion (cost of congestion)
  basic congestion control alg.
  TCP/Reno congestion control
    design
    analysis

## Slide 8: Objective
To understand
  the throughput of TCP/Reno as a function of RTT (RTT), loss rate (p) and packet size
  the underlying queue dynamics
We will analyze TCP/Reno under two different setups

## Slide 9
TCP/Reno Throughput Analysis
Given mean packet loss rate p, mean round-trip time RTT, packet size S
Consider only the congestion avoidance mode (long flows such as large files)
Assume no timeout
Assume mean window size is Wm segments, each with S bytes sent in one RTT:
Throughput =
Wm * S
RTT
bytes/sec

## Slide 10
Outline
Admin and recap
Transport congestion control
  what is congestion (cost of congestion)
  basic congestion control alg.
  TCP/Reno congestion control
    design
    analysis
      small fish in a big pond
        loss rate given from the environment

## Slide 11
TCP/Reno Throughput Modeling (Fixed, Given Loss Rate)
=>
=>
This is called the TCP throughput sqrt of loss rate law.

## Slide 12: Exercise: Application of Analysis
State of art network link can reach 100 Gbps. Assume packet size 1250 bytes, RTT 100 ms, what is the highest packet loss rate to still reach 100 Gbps?
tcp-reno-tput.xlsx

## Slide 13
Outline
Admin and recap
Transport congestion control
  what is congestion (cost of congestion)
  basic congestion control alg.
  TCP/Reno congestion control
    design
    analysis
      small fish in a big pond
      big fish in small pond
        growth causes losses

## Slide 14
TCP/Reno Throughput Modeling: Relating W with Loss Rate p
Time
cwnd
congestion
avoidance
TD
ssthresh
Total packets sent per cycle = (W/2 + W)/2 * W/2 = 3W2/8
W/2
W
Assume one loss per cycle
=> p = 1/(3W2/8) = 8/(3W2)
=>

## Slide 15: A Puzzle: cwnd and Rate of a TCP Session
Question: although cwnd fluctuates widely (i.e., cut to half), why can the sending rate stay relatively smooth?

## Slide 16
TCP/Reno Queueing Dynamics
Time
cwnd
congestion
avoidance
TD
ssthresh
bottleneck
bandwidth
filling buffer
draining buffer
If the buffer at the bottleneck is large enough, the buffer is never empty (not idle), during the cut-to-half to “grow-back” process.
Exercise: How big should the buffer be to achieve full utilization?

## Slide 17: Extreme: Zero Buffer
Assume
  BW: 10 G
  RTT: 100 ms
  Packet: 1250 bytes
  BDP (full window size): 100,000 packets
A loss can cut window size from 100,000 to 50,000 packets
To fully grow back
  Need 50,000 RTTs => 5000 seconds, 1.4 hours
Q: What is the link utilization in one cycle?

## Slide 18: Design
Assume a generic AIMD alg:
  increase to W + after each successful RTT
  reduce to β W after each loss event
Q: What value β gives higher utilization (assume small/zero buffer)?
Q: Assume picking a high value β, how to make the alg TCP friendly (same throughput as =1, β=0.5)?

## Slide 19
Generic AIMD and TCP Friendliness
Time
cwnd
congestion
avoidance
TD
ssthresh
Total packets sent per cycle =
βW
W
Assume one loss per cycle
=
p =
tput =
w=
=
=
TCP friendly =>

## Slide 20
Outline
Admin and recap
Transport congestion control
  what is congestion (cost of congestion)
  basic congestion control alg.
  TCP/Reno congestion control
  TCP Cubic

## Slide 21: TCP Cubic
Designed in 2008
Default for Linux
Most sockets in MAC appear to use cubic as well
  sw_vers
  sysctl –a

## Slide 22: TCP Cubic Goals
Improve TCP efficiency over fast, long-distance links
TCP friendliness
Fairness of flows w/ different RTTs
Window growth depends on real-time (from congestion- epoch through synchronized losses)
Smaller reduction, longer stay at BDP, faster than linear increase---cubic function
Follows TCP if TCP gives higher rate

## Slide 23: TCP BIC Algorithm
Setting
  Wmax = cwnd size before reduction
    Too big
  Wmin = β*Wmax – just after reduction, where β is multiplicative decrease factor
    Small
Basic idea
  binary search between Wmax and Wmin
Time
cwnd
CA
TD
Wmin
TD
TD
TD
Wm
CA
CA
CA
Wmax

## Slide 24: TCP BIC Algorithm: Issues
  Pure binary search (jump from Wmin to (Wmax and Wmin)/2) may be too aggressive
  Use a large step size Smax
What if you grow above Wmax?
  Use binary growth (slow start) to probe more
Time
cwnd
CA
TD
Wmin
TD
TD
TD
Wm
CA
CA
CA
Wmax

## Slide 25: TCP BIC Algorithm
Packet loss event
Wmax
Wmin = β*Wmax
midpoint = (Wmin + Wmax)/2
midpoint – Wmin > Smax
Wmin + Smax
Wmin
midpoint = (Wmin + Wmax)/2
Wmin + Smax
Wmin
Additive Increase
midpoint = (Wmin + Wmax)/2
Wmin + Smin
Wmin
(midpoint – Wmin)< Smin
Binary Search
Wmax + Smin
Wmax + Smin
Wmax +Smax
Slow Start
Wmax + 2Smax
Wmax + 3Smax
Additive Inc.
Max Probing

## Slide 26: TCP BIC Algorithm
  while (cwnd < Wmax) {
  if ( (midpoint - Wmin) > Smax )
      cwnd = cwnd + Smax
      else
      if ((midpoint - Wmin) < Smin)
      cwnd = Wmax
      else
      cwnd = midpoint
      if (no packet loss)
      Wmin = cwnd
      else
      Wmin = β*cwnd
      Wmax = cwnd
      midpoint = (Wmax + Wmin)/2
    }
Additive Increase
Binary Search

## Slide 27: TCP BIC Algorithm: Probe
  while (cwnd >= Wmax){
  if (cwnd < Wmax + Smax)
    cwnd = cwnd + Smin
    else
    cwnd = cwnd + Smax
    if (packet loss)
    Wmin = β*cwnd
    Wmax = cwnd
  }
Slow growth
Fast growth
Max Probing

## Slide 28: TCP BIC - Summary
Packet loss event
Binary Increase
Additive Increase
Slow
Start
Max Probing
+ Smax
Time
Additive Increase
Wmax
jump to midpoint
+ Smin
+ Smax

## Slide 29: TCP BIC in Action

## Slide 30: TCP BIC Analysis
Advantages
  Faster convergence at large gap
  Slower growth at convergence to avoid timeout
Issues
  Still depend on RTT
  Complex growth function
More details: http://www.land.ufrj.br/~classes/coppe-redes-2007/projeto/BIC-TCP-infocom-04.pdf

## Slide 31: Cubic High-Level Structure
If (received ACK && state == cong avoid)
  Compute Wcubic(t+RTT).
  If cwnd < WTCP
    Cubic in TCP mode
  If cwnd < Wmax
    Cubic in concave region
  If cwnd > Wmax
    Cubic in convex region

## Slide 32: The Cubic function
where C is a scaling factor, t is the elapsed time from the last window reduction, and β is a constant multiplication decrease factor
concave region
convex region
slow down
Wtcp(t)

## Slide 34
Outline
Admin and recap
Transport congestion control
  what is congestion (cost of congestion)
  basic congestion control alg.
  TCP/Reno congestion control
  TCP Cubic
  TCP/Vegas

## Slide 35: TCP/Vegas (Brakmo & Peterson 1994)
SS
time
window
CA
Idea: try to detect congestion by delay before loss
Objective: not to overflow the buffer; instead, try to maintain a constant number of packets in the bottleneck queue

## Slide 36: TCP/Vegas: Key Question
How to estimate the number of packets queued in the bottleneck queue?
SS
time
window
CA

## Slide 37: Recall: Little’s Law
For any system with no or (low) loss.
Assume
  mean arrival rate X, mean service time T, and mean number of requests in the system W
Then relationship between W, X, and T:
T, W
X
Notes: Proof of Little’s Law:

## Slide 38: Estimating Number of Packets in the Queue

## Slide 39: TCP/Vegas CA algorithm
T = Tprop + Tqueueing
Applying Little’s Law:
xvegas T = xvegas Tprop + xvegas Tqueueing, where xvegas = W / T is the sending rate
Then number of packets in the queue is xvegas Tqueueing = xvegas T - xvegas Tprop
= W – W/T Tprop

## Slide 40: TCP/Vegas CA algorithm
queue size
for every RTT
{ if W – W/RTT RTTmin < a then W ++
if W – W/RTT RTTmin > a then W -- }
for every loss
W := W/2
SS
time
window
CA
maintain a constant number of packets in the bottleneck buffer

## Slide 41: Discussions
If two flows, one TCP Vegas and one TCP reno run together, how may bandwidth partitioned among them?
Issues that limit Vegas deployment?