## Slide 1: Network Transport Layer: Network Resource Allocation Framework
  Qiao Xiang, Congming Gao, Qiang Su
  https://sngroup.org.cn/courses/cnns-xmuf25/index.shtml
11/13/2025
This deck of slides are heavily based on CPSC 433/533 at Yale University, by courtesy of Dr. Y. Richard Yang.

## Slide 2
Outline
Admin and recap
Transport congestion control
  what is congestion (cost of congestion)
  basic congestion control alg.
  TCP/Reno congestion control
  TCP Cubic
  TCP/Vegas
  network wide resource allocation
    general framework
    objective function: axiom derivation of network-wide objective function
    algorithm: general distributed algorithm framework
    application: TCP/Reno TCP/Vegas revisited
2

## Slide 3
Recap: TCP/Reno Throughput Modeling
=>
=>
This is called the TCP throughput sqrt of loss rate law.
3

## Slide 4
Recap: TCP/Reno Throughput Modeling
Time
cwnd
congestion
avoidance
TD
ssthresh
Total packets sent per cycle = (W/2 + W)/2 * W/2 = 3W2/8
W/2
W
Assume one loss per cycle
=> p = 1/(3W2/8) = 8/(3W2)
=>

## Slide 5
Recap: Generic AIMD and TCP Friendliness
Time
cwnd
congestion
avoidance
TD
ssthresh
Total packets sent per cycle =
βW
W
Assume one loss per cycle
=
p =
tput =
w=
=
=
TCP friendly =>

## Slide 6: TCP/Vegas (Brakmo & Peterson 1994)
SS
time
window
CA
Idea: try to detect congestion by delay before loss
Objective: not to overflow the buffer; instead, try to maintain a constant number of packets in the bottleneck queue

## Slide 7: TCP/Vegas: Key Question
How to estimate the number of packets queued in the bottleneck queue?
SS
time
window
CA

## Slide 8: Recall: Little’s Law
For any system with no or (low) loss.
Assume
  mean arrival rate X, mean service time T, and mean number of requests in the system W
Then relationship between W, X, and T:
T, W
X
Notes: Proof of Little’s Law:

## Slide 9: TCP/Vegas CA algorithm
T = Tprop + Tqueueing
Applying Little’s Law:
xvegas T = xvegas Tprop + xvegas Tqueueing, where xvegas = W / T is the sending rate
Then number of packets in the queue is xvegas Tqueueing = xvegas T - xvegas Tprop
= W – W/T Tprop

## Slide 10: TCP/Vegas CA algorithm
queue size
for every RTT
{ if W – W/RTT RTTmin < a then W ++
if W – W/RTT RTTmin > a then W -- }
for every loss
W := W/2
SS
time
window
CA
maintain a constant number of packets in the bottleneck buffer

## Slide 11: Discussions
If two flows, one TCP Vegas and one TCP reno run together, how may bandwidth partitioned among them?
Issues that limit Vegas deployment?

## Slide 12
Outline
Admin and recap
Transport congestion control
  what is congestion (cost of congestion)
  basic congestion control alg.
  TCP/Reno congestion control
  TCP Cubic
  TCP/Vegas
  network wide resource allocation
    general framework
12

## Slide 13
Motivation
So far our discussion is implicitly on a network with a single bottleneck link; this simplifies design and analysis:
  efficiency/optimality (high utilization)
    fully utilize the bandwidth of the link
  fairness (resource sharing)
    each flow receives an equal share of the link’s bandwidth

## Slide 14
Network Resource Allocation
It is important to understand and design protocols for a general network topology
  how will TCP allocate resource in a general topology?
  how should resource be allocated in a general topology?

## Slide 15
Example: TCP/Reno Rates
x1
x2
x3
Rates: x1 = = 0.26
x2 = x3 = 0.74
C= 1
C = 1

## Slide 16
Example: TCP/Vegas Rates
x1
x2
x3
Rates : x1 = 1/3
x2 = x3 = 2/3
C= 1
C = 1

## Slide 17
Example: Max-min Fairness
Max-min fairness: maximizes the throughput of the flow receiving the minimum (of resources)
    Justification: John Rawls, A Theory of Justice (1971)
      http://en.wikipedia.org/wiki/John_Rawls
    This is a resource allocation scheme used in ATM and some other network resource allocation proposals
17

## Slide 18
Example: Max-Min
x1
x2
x3
Rates: x1 = x2 = x3 = 1/2
C= 1
C = 1

## Slide 19
Framework: Network Resource Allocation Using Utility Functions
A set of flows F
Let xf be the rate of flow f, and the utility to flow f is Uf(xf).
Maximize aggregate utility, subject to capacity constraints

## Slide 20
Example: Maximize Throughput
x1
x2
x3
Optimal: x1 = 0
x2 = x3 = 1
C= 1
C = 1

## Slide 21
Example: Proportional Fairness
x1
x2
x3
Optimal: x1 = 1/3
x2 = x3 = 2/3
C= 1
C = 1

## Slide 22
Example 3: a “Funny” Utility Function
x1
x2
x3
Optimal: x1 = = 0.26 x2 = x3 = 0.74
C= 1
C = 1

## Slide 23: Summary: Allocations
Objective | Allocation (x1, x2, x3) |  | 
TCP/Reno | 0.26 | 0.74 | 0.74
TCP/Vegas | 1/3 | 2/3 | 2/3
Max Throughput | 0 | 1 | 1
Max-min | ½ | ½ | ½
Max sum log(x) | 1/3 | 2/3 | 2/3
Max sum of -1/(RTT2 x) | 0.26 | 0.74 | 0.74
x1
x2
x3
C= 1
C = 1

## Slide 24: Questions
Forward engineering: systematically
  design objective function
  design distributed alg to achieve objective
Science/reverse engineering: what do TCP/Reno, TCP/Vegas achieve?
Objective | Allocation (x1, x2, x3) |  | 
TCP/Reno | 0.26 | 0.74 | 0.74
TCP/Vegas | 1/3 | 2/3 | 2/3
Max throughput | 0 | 1 | 1
Max-min | ½ | ½ | ½
Max sum log(x) | 1/3 | 2/3 | 2/3
Max sum of -1/(RTT2 x) | 0.26 | 0.74 | 0.74

## Slide 25
Outline
Admin and recap
Transport congestion control
  what is congestion (cost of congestion)
  basic congestion control alg.
  TCP/Reno congestion control
  TCP Cubic
  TCP/Vegas
  network wide resource allocation
    general framework
    objective function: an example of an axiom derivation of network-wide objective function
25

## Slide 26: Network Bandwidth Allocation Using Nash Bargain Solution (NBS)
High level picture
  given the feasible set of bandwidth allocation, we want to pick an allocation point that is efficient and fair
The determination of the allocation point should be based on “first principles” (axioms)

## Slide 27: Network Bandwidth Allocation: Feasible Region
x1
x2
x3
C= 1
C = 1
x1
x3
x2

## Slide 28: Nash Bargain Solution (NBS)
R
s
x1
x2
Assume a finite, convex feasible set in the first quadrant
Axioms
Notes: The second two enforce consistency across scenarios

## Slide 29: Nash Bargain Solution (NBS)
R
T
s
x1
x2
Assume a finite, convex feasible set in the first quadrant
Axioms
  Pareto optimality
    impossibility of increasing the rate of one user without decreasing the rate of another
  symmetry
    a symmetric feasible set yields a symmetric outcome
  invariance of linear transformation
    the allocation must be invariant to linear transformations of users’ rates
  independence of irrelevant alternatives
    assume s is an allocation when feasible set is R, s T  R, then s is also an allocation when the feasible set is T
Notes: The second two enforce consistency across scenarios

## Slide 30: Nash Bargain Solution (NBS)
Surprising result by John Nash (1951)
  the rate allocation point is the feasible point which maximizes
This is equivalent to maximize
In other words, assume each flow f has utility function log(xf)
I will give a proof for F = 2
  think about F > 2
R
x1
x2

## Slide 31: Nash Bargain Solution
s
x1 * x2
Assume s is the feasible point which maximizes x1 * x2
Scale the feasible set so that s is at (1, 1)
  how?
x2
x1
1
1

## Slide 32: Nash Bargain Solution
x1 = x2
s
x1 + x2 = 2
x1 * x2 = 1
Question: after the transformation, is there any feasible point with x1 + x2 > 2?
P
Q
x1
x2
R
1
1

## Slide 33: Nash Bargain Solution
x1 = x2
s
x1 + x2 = 2
x1 * x2 = 1
Consider the symmetric rectangle U containing the now feasible set
-> According to symmetry and Pareto, s is the allocation when feasible set is U
According to independence of irrelevant alternatives, the allocation of R is s as well.
x1
x2
R
1
1
U

## Slide 34
Allocation is proportionally fair if for any other allocation, aggregate of proportional changes is non-positive, e.g. if xf is a proportional-fair allocation, and yf is any other feasible allocation, then require

## Slide 35: Questions to Think
Vary the axioms and see if you can derive any objective functions

## Slide 36
Outline
Admin and recap
Transport congestion control
  what is congestion (cost of congestion)
  basic congestion control alg.
  TCP/Reno congestion control
  TCP Cubic
  TCP/Vegas
  network wide resource allocation
    general framework
    objective function: an example axiom derivation of network-wide objective function
    algorithm: general distributed algorithm framework
    application: TCP/Reno TCP/Vegas revisited
36

## Slide 37
Recall: Resource Allocation Framework
The Resource-Allocation Problem:
Goal: Design a distributed alg to solve the problem.
Discussion：
  What are typical approaches to solve optimization, e.g.,? max U(x)
  Why is the Resource-Allocation problem hard to solve by a distributed algorithm?

## Slide 38: A Two-Slide Summary of Constrained Convex Optimization Theory
g(x)
f(x)
f(x) concave
g(x) linear
S is a convex set
q
S
Map each x in S, to [g(x), f(x)]
For each slope q (>=0), computes f(x) – q g(x) of all mapped [f(x), g(x)]
q
Top contour of map is concave
Easy to read solution from contour
Notes: The intersection w/ y-axis is f(x)-qg(x)
Important to draw the two cases of g(x)

## Slide 39: A Two-Slide Summary of Constrained Convex Optimization Theory
g(x)
f(x)
f(x) concave
g(x) linear
S is a convex set
q1
q2
S
D(q) is called the dual; q (>= 0) are called prices in economics
- According to optimization theory: when D(q) achieves minimum over all q (>= 0), then the optimization objective is achieved.
D(q) provides an upper bound on obj.
q3

## Slide 40
Dual of the Primal
x1
x2
x3
1
1

## Slide 41: Dual of the Primal
x1
x2
x3
1
1

## Slide 42: Distributed Optimization: User Problem
Given pf (=sum of dual var ql along the path) flow f chooses rate xf to maximize:
Using the price signals, the optimization problem of each user is independent of each other!

## Slide 43: Distributed Optimization: User Problem
At equilibrium (i.e., at optimal), xf satisfies:
How should flow f adjust xf locally?

## Slide 44: Interpreting Congestion Measure
xf(t)
ql(t)
q2(t)

## Slide 45: Distributed Optimization: Network Problem
The network (i.e., link l) adjusts the link signals ql (assume after all flows have picked their optimal rates given congestion signal)

## Slide 46: Distributed Optimization: Network Problem
how should link l adjust ql locally?

## Slide 47
System Architecture
SYSTEM(U):
USERf:
NETWORK:

## Slide 48
Decomposition Theorem
There exist vectors p , w and x such that
  wf = pfxf for f  F
  wf solves USERf(Uf; pf)
  x solves NETWORK(w)
The vector x then also solves SYSTEM(U).

## Slide 49
Outline
Admin and recap
Transport congestion control
  what is congestion (cost of congestion)
  basic congestion control alg.
  TCP/Reno congestion control
  TCP Cubic
  TCP/Vegas
  network wide resource allocation
    general framework
    objective function: an example axiom derivation of network-wide objective function
    algorithm: a general distributed algorithm framework
    application: TCP/Reno and TCP/Vegas revisited
49

## Slide 50
TCP/Reno Dynamics
= 1
=
=)

## Slide 51
TCP/Reno Dynamics
=)

## Slide 52
TCP/Vegas Dynamics
= -)
)
))

## Slide 53
TCP/Vegas Dynamics
))

## Slide 54: Summary: TCP/Vegas and TCP/Reno
Pricing signal is queueing delay Tqueueing
Pricing signal is loss rate p

## Slide 55: Discussion
Assume that you are given a set of flows deployed at a given network topology.
What is a simple way to predict TCP rate allocation?

## Slide 56: Summary: Resource Allocation Frameworks
Forward (design) engineering:
  how to determine objective functions
  given objective, how to design effective alg
Reverse (understand) engineering:
  understand current protocols (what are the objectives of TCP/Reno, TCP/Vegas?)
Additional pointers:
  http://www.statslab.cam.ac.uk/~frank/pf/