## Slide 1: Network Layer: Global Internet Routing (Interdomain, BGP); DHCP; Forwarding
Qiao Xiang, Congming Gao, Qiang Su
  https://sngroup.org.cn/courses/cnns-xmuf25/index.shtml
11/27/2024
This deck of slides are heavily based on CPSC 433/533 at Yale University, by courtesy of Dr. Y. Richard Yang.

## Slide 2
Outline
Admin and recap
Network control plane
  Routing
    Routing computation
      Basic routing computation protocols
        Distance vector protocols (distributed computing)
        Link state protocols (distributed state synchronization)
      Global Internet routing

## Slide 3
Recap: Routing Context
Often depends on a graph abstraction:
graph nodes are routers
graph edges are physical links
  links have properties: delay, capacity, $ cost, policy
Goal: determine “good” paths
(sequences of routers) thru
networks from source to dest.
Routing
A
E
D
C
B
F
2
2
1
3
1
1
2
5
3
5

## Slide 4: Recap: Link-State Routing
Basic idea: Not distributed computing, only distributed state distribution
Net topology, link costs are distributed to all nodes
    all nodes have same info
    Each node computes its shortest paths from itself to all other nodes
      standard Dijkstra’s algorithm as path compute alg
      Allows multiple same-cost paths
      Multiple cost metrics per link (for type of service routing)
Most commonly used routing protocol (e.g., OSPF/ISIS) by most networks in Internet

## Slide 5: Roadmap: Routing Computation Architecture Spectrum
Datapath
Distributed Bellman Ford
Distributed Link State
Dijkstra
Datapath
Distributed Bellman Ford
Datapath
Distributed Bellman Ford
Distributed Link State
Distributed Link State
Dijkstra
Dijkstra
Notes: RIP: 1988 RFC1058 OSFPv2: RFC2328

## Slide 6
b
a
AS C
(RIP intra
routing)
c
AS B
(OSPF intra
routing)
AS A
(OSPF intra
routing)
eBGP
iBGP
Gateway routers participate in intradomain to learn internal routes.
Gateway routers of diff. auto. systems exchange routes using eBGP
Gateway routers of same AS share learned external routes using iBGP.
i
e
f
g
h
d
Inter-AS routers form an overlay
Recap: Routing with Autonomous Systems

## Slide 7
Recap: BGP Basic Operations
BGP is a Path Vector protocol
  similar to Distance Vector protocol
  a border gateway sends to a neighbor entire path (i.e., a sequence of ASNs) to a destination, e.g.,
    gateway X sends to neighbor N its path to dest. Z:
path (X,Z) = X,Y1,Y2,Y3,…,Z
  if N selects path(X, Z) advertised by X, then: path (N,Z) = N, path (X,Z)
X
N
Z

## Slide 8
Outline
Admin and recap
Network control plane
  Routing
    Link weights assignment
    Routing computation
      Basic routing computation protocols
      Global Internet routing
        Basic architecture
        BGP (Border Gateway Protocol): The de facto Inter-domain routing standard
          Basic operations
          BGP as a policy routing framework (control interdomain routes)

## Slide 9: BGP Policy Routing Framework: Decision Components
routing cache
select best path
export path to neighbors
route selection policy: rank paths
export policy: which paths export to which neighbors
Yale
Qwest
AT&T
Internet2
1 3 0
1 0
9

## Slide 10: BGP Example (1)
AS A
(OSPF)
AS B
(OSPF intra
routing)
AS D
AS C
i
b
b->i: I can reach hosts
in D; my path: BCD
a1
a2
d
d->a2: I can reach
hosts in D; my path: D
a1->i: I can reach hosts in D; my path: AD
E
F
Export to E: i->e: I can reach hosts in D; path: IAD
AS I
a2->a1: I can reach
hosts in D; path: D
Route selection policy:
- Shortest AS Path policy:
b->i2: I can reach hosts
in D; my path: BCD
i2
i2->i: I can reach hosts in D; path: BCD
No export to F (effect?)
Choose AD using a1
Export policy controls ingress, i.e., who can use I
Notes: Choose

## Slide 11: BGP Example (2)
AS A
(OSPF)
AS B
(OSPF intra
routing)
AS D
AS C
i
b
b->i: I can reach hosts
in D; my path: BCD
a1
a2
d
d->a2: I can reach
hosts in D; my path: D
a1->i: I can reach hosts in D; my path: AD
E
F
Export to E: i->e: I can reach hosts in D; path: IBCD
AS I
a2->a1: I can reach
hosts in D; path: D
Selection policy: - Low local_pref for A
- Shortest AS Path
- Prefer eBGP
b->i2: I can reach hosts
in D; my path: BCD
i2
i2->i: I can reach hosts in D; path: BCD
Outcome: Choose BCD using b
Called hot potato (why?)
Notes: Choose

## Slide 12: BGP Example (3)
AS A
(OSPF)
AS B
(OSPF intra
routing)
AS D
AS C
i
b
b->i: I can reach hosts
in D; my path: BCD
a1
a2
d
d->a2: I can reach
hosts in D; my path: D
a1->i: I can reach hosts in D; my path: AD
E
F
Export to E: i->e: I can reach hosts in D; path: IBCD
AS I
a2->a1: I can reach
hosts in D; path: D
Selection policy: - Low local pref A
- Shortest AS Path
- Prefer iBGP
b->i2: I can reach hosts
in D; my path: BCD
i2
i2->i: I can reach hosts in D; path: BCD
Outcome: Choose BCD using i2
Called cold potato (why?)
Notes: Choose

## Slide 13: Observing BGP Paths
Using one of the looking glass servers: http://www.bgp4.as/looking-glasses
https://www.gin.ntt.net/looking-glass/

## Slide 14
Outline
Admin and recap
Network control plane
  Routing
    Link weights assignment
    Routing computation
      Basic routing computation protocols
      Global Internet routing
        Basic architecture
        BGP (Border Gateway Protocol): The de facto Inter-domain routing standard
          Basic operations
          BGP as a policy routing framework (control interdomain routes)
          Policy/interdomain routing analysis

## Slide 15
Motivation: Policy Routing Stability
2
0
3
1
2 1 0
2 0
1 3 0
1 0
3 2 0
3 0
4
3
preferred
less
preferred
The BAD GADGET example:
- 0 is the destination
- the route selection policy of each AS is to prefer its counter clock-wise neighbor
Policy (preferences) aggregation fails: routing instability !
A policy routing system can be considered as a system to aggregate local preferences, but aggregation may not be always successful.

## Slide 16: General Framework of Preference Aggregation
Also called Social Choice
  Given individual preferences, define a framework to aggregate individual preferences:
    A set of choices: a, b, c, …
    A set of voters 1, 2, …
      Each voter has a preference (ranking) of all choices, e.g.,
        voter 1: a > b > c
        voter 2: a > c > b
        voter 3: a > c > b
    A well-specified aggregation rule (protocol) computes an aggregation of ranking, e.g.,
      Society (network): a > b > c
For more details: see Semih Salihoglu (2007). Interdomain Routing as a Social Choice.
Notes: https://en.wikipedia.org/wiki/Arrow%27s_impossibility_theorem

## Slide 17: Example: Aggregation of Global Preference
S
A
B
D
Choices (for S->D route): SAD, SBD, SABD, SBAD
Voters S, A, B, D
Each voter has a preference, e.g.,
  S: SAD > SBD > SABD > SBAD
  …
Notes: https://en.wikipedia.org/wiki/Arrow%27s_impossibility_theorem

## Slide 18: Arrow’s Impossibility Theorem
Axioms:
  Transitivity
    if a > b & b > c, then a > c
  Unanimity:
    If all participants prefer a over b (a > b) => a > b
  Independence of irrelevant alternatives (IIA)
    Social ranking of a and b depends only on the relative ranking of a and b among all participants
Result:
  Arrow’s Theorem: Any constitution that respects transitivity, unanimity and IIA is a dictatorship.
Notes: https://en.wikipedia.org/wiki/Arrow%27s_impossibility_theorem

## Slide 19: Proofs of Arrow’s Theorem
There are quite a few proofs, and the six-page paper linked on the Schedule page gives three simple proofs.
Below, I give the key insight of the proof using approach 1.

## Slide 20: The Extremal Lemma
Let choice b be chosen arbitrarily. Assume that every voter puts b at the very top or the very bottom of his ranking. Then society must as well (even if half voters put b at the top and half at the bottom)
Proof: by contradiction.
  Assume there exist a and c such that society has a >= b; b >= c.
    By transitivity, a >= c
  We can move c above a w/o changing ab or cb votes, leading to c > a
    By unanimity, c > a

## Slide 21: Step 1: Existence of Pivotal Voter
Let choice b be chosen arbitrarily. There exist a voter n* = n(b) who is extremely pivotal for b in the sense that by changing his vote at some profile, he can move b from the very bottom to the very top in the social ranking.
Proof:
  Consider an extreme profile where b is at the bottom of each voter.
  Consider voter from 1 to n, and we move b from bottom to top one-by-one.
  The first voter whose change causes b to move to the top is n*
    By unanimity, this change must happen at the latest when n*=n

## Slide 22: Step 2: n*=n(b) is dictator of any pair ac not involving b
Proof
  Consider a from ac pair. We show that if a >n* c, then constitution protocol has a > c
  Let profile before n* moves b to top as profile I
  Let profile after n* moves b to top as profile II
  Construct profile III from II by letting n* move a above b; all others can arrange ac as they want, but leave b in extreme position
    a>b in profile I, and a,b is equivalent by IIA in profiles I and III
    b>c in profile II, and bc is equivalent by IIA in profiles II and III
b
.
.
.
b
.
.
.
.
.
.
b
.
.
.
b
.
.
.
b
b
.
.
.
b
.
.
.
b
.
.
.
.
.
.
b
.
.
.
b
1 2 n* . N
b
.
.
.
b
.
.
.
a
b
.
c
.
.
.
b
.
.
.
b
Constitution protocol: b bottom
Constitution protocol : b top
Profile I
Profile II
Profile III
Constitution protocol: a > b since ab same as I
b > c since bc same as II

## Slide 23: Step 3: n* is dictator for every pair ab
Consider c not equal to a or b
There exists n(c) who is a dictator of any pair not involving c, such as the pair ab, i.e.,
  For any profile, if a >n(c) > b, a > b in constitution protocol
n(c) must be n*
  Assume not.
    Consider Profile I and Profile II.
    Since n(c) is not n*, n(c) ranking of ab does not change in Profile I and Profile II.
    When n* changes ab ranking between Profile I and Profile II, the global ranking of ab changes.
    Contradiction.

## Slide 24
Outline
Admin and recap
Network control plane
  Routing
    Link weights assignment
    Routing computation
      Basic routing computation protocols
      Global Internet routing
        Basic architecture
        BGP (Border Gateway Protocol): The de facto Inter-domain routing standard
          Basic operations
          BGP as a policy routing framework (control interdomain routes)
          Policy/interdomain routing analysis
            Global preference aggregation and Arrow’s Theorem [Optional]
            Local preference aggregation

## Slide 25: BGP w/ Local Preference
BGP preferences are typically local (only on paths start from itself)
Hence the preferences have dependency (priority)
  The “closer” a node to the destination, the more “powerful” it may be
2 1 0
2 0
1 0
3 0
1 3 0
3 2 0
2
0
1
3
320
30
210
20
130
10
25

## Slide 26: Complete Dependency: P-Graph
Complete dependency can be captured by a structure called P-graph
Nodes in P-graph are feasible paths
Edges represent priority (low to high)
  A directed edge from path N1P1 to P1
    intuition: to let N1 choose N1P1, P1 must be chosen and exported to N1
  A directed edge from a lower ranked path to a higher ranked path
    intuition: the higher ranked path should be considered first
2 1 0
2 0
1 0
3 0
1 3 0
3 2 0
2
0
1
3
320
30
210
20
130
10
Any observation on the P-graph?
26

## Slide 27: P-Graph and BGP Convergence
If the P-graph of the networks has no loop, then policy routing converges.
  intuition: choose the path node from the partial order graph with no out-going edge to non-fixed path nodes, fix the path node, eliminate all no longer feasible; continue
Example: suppose we swap the order of 30 and 320
2 1 0
2 0
1 0
3 0
1 3 0
3 2 0
2
0
1
3
30
320
210
20
130
10
27

## Slide 28
Outline
Admin and recap
Network control plane
  Routing
    Link weights assignment
    Routing computation
      Basic routing computation protocols
      Global Internet routing
        Basic architecture
        BGP (Border Gateway Protocol): The de facto Inter-domain routing standard
          Basic operations
          BGP as a policy routing framework (control interdomain routes)
          Policy/interdomain routing analysis
            Global preference aggregation and Arrow’s Theorem
            Local preference aggregation
            Economics and interdomain routing patterns

## Slide 29
Internet Economy: Two Types of Business Relationship
Customer provider relationship
  a provider is an AS that connects the customer to the rest of the Internet
  customer pays the provider for the transit service
  e.g., XMU is a customer of CERNET and China Telecom
Peer-to-peer relationship
  mutually agree to exchange traffic between their respective customers only
  there is no payment between peers
provider
customer
peer
peer
provider
provider to
customer
29

## Slide 30: Route Selection Policies and Economics
Route selection (ranking) policy:
  the typical route selection policy is to prefer customers over peers/providers to reach a destination, i.e., Customer > pEer/Provider
provider
customer
peer
30

## Slide 31
customer
provider
customer
peer
Export Policies and Economics
provider
provider
customer
peer
peer
provider
customer
peer
Routes learned from a customer are sent to all other neighbors
Routes learned from a provider are sent only to customers
Routes learned from a peer are sent only to customers
case 1: routes learned from customer
case 2: routes learned from provider
case 3: routes learned from peer
31

## Slide 32
Example: Typical Export -> No-Valley Routing
P1
A
P2
IP traffic
A advertises path to C, but not P2
A advertises to C paths to P1 and P2
A advertises path to C, but not P1
Suppose P1 and P2 are providers of A; A is a provider of C
C
A learns paths to C, P1, P2
32

## Slide 33: Typical Export Policies Route Patterns
Assume a BGP path SABCD to destination AS D. Consider the business relationship between each pair:
Three types of business relationships:
  PC (provider-customer)
  CP (customer-provider)
  PP (peer-peer)
S A B C D

## Slide 34: Typical Export Policies Route Patterns
Invariant 1 of valid BGP routes (with labels representing business relationship)
P C
?
P C
P C
Dest
P C
Reasoning: only route learned from customer is sent to provider; thus
after a PC, it is always PC to the destination
Notes: If PC, then PC all the way to destination
If CP/PP, all preceding is CP

## Slide 35: Typical Export Policies Route Patterns
Invariant 2 of valid BGP routes (with labels representing business relationship)
CP
?
CP
CP
······
Dest
Reasoning: routes learned from peer or provider are sent to only customers; thus all relationship before is CP.
/PP
Notes: If PC, then PC all the way to destination
If CP/PP, all preceding is CP

## Slide 36: Stability of BGP Policy Routing
Suppose
  there is no loop formed by provider-customer relationship in the Internet
  each AS uses typical route selection policy:
    C > E/P
  each AS uses the typical export policies
Then policy routing always converges (i.e., is stable).

## Slide 37: Case 1: A Link is PC
PC
Proof by contradiction. Assume a loop in P-graph. Consider a fixed link. in the loop
PC
PC
AS 1
AS 2
AS 3
AS 4

## Slide 38: Case 2: Link is CP/PP
CP/PP
CP/PP
CP
CP/PP
CP
AS 1
AS 2
AS 3
AS 4

## Slide 39
Summary: BGP Policy Routing
Advantage
  satisfies current demand
Issues
  policy dispute can lead to instability
    current Internet economy provides a stability framework, but if the framework changes, we may see instability
  Hierarchical routing can be inefficient
AS 4
AS 3
AS 2
AS 1

## Slide 40: Routing: Remaining Issue
AS A
(OSPF)
AS B
(OSPF intra
routing)
AS D
AS C
i
b
Naïve design is to send individual host D’s IP. Can we do better?
a1
a2
d
a1->i: I can reach
hosts in D; my path: AD
E
F
AS I
d1
d2
Notes: How to specify hosts in D

## Slide 41
Outline
Admin and recap
Network control plane
  Routing
    Link weights assignment
    Routing computation
      Basic routing computation protocols
      Global Internet routing
        Basic architecture
        BGP (Border Gateway Protocol): The de facto Inter-domain routing standard
          Basic operations
          BGP as a policy routing framework (control interdomain routes)
          Policy/interdomain routing analysis
            Global preference aggregation and Arrow’s Theorem
            Local preference aggregation
            Economics and interdomain routing patterns
          IP addresses for Interdomain routing

## Slide 42: IP Addressing Scheme: Requirements
Uniqueness: We need an address to uniquely identify each destination
Aggregability : Routing scalability needs flexibility in aggregation of destination addresses
  we want to aggregate as a large set of destinations as possible in BGP announcements
Current: the unit of routing in the Internet is a classless interdomain routing (CIDR) address

## Slide 43
IP Address: Uniqueness
IPv4 address: A 32-bit unique identifier for an interface
interface:
  routers typically have multiple interfaces
  host may have multiple interfaces
  %/sbin/ifconfig -a
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
223.1.3.2 = 11011111 00000001 00000011 00000010
223
1
2
3
e.g., /etc/sysconfig/network-scripts/ifcfg-enp0s25
%ifup

## Slide 44: IP Addressing: Class-ful Addressing
given notion of “network”, let’s re-examine IP addresses:
“class-ful” addressing in the original IP design:
1.0.0.0 to
127.255.255.255
128.0.0.0 to
191.255.255.255
192.0.0.0 to
223.255.255.255
224.0.0.0 to
239.255.255.255
240.0.0.0 to
255.255.255.255

## Slide 45: Classless InterDomain Routing (CIDR) Address: Aggregation
A CIDR address partitions an IP address into two parts
  A prefix representing the network portion, and the rest (host part)
  address format: a.b.c.d/x, where x is # bits in network portion of address
11001000 00010111 00010000 00000000
network
part
host
part
200.23.16.0/23
Some systems use mask (1’s to indicate network bits), instead of the /x format

## Slide 46: CIDR Aggregation in BGP
AS A
(OSPF)
AS D
i
a1
a2
d
i->a1: I can reach
130.132.0/22; my path: I
AS I
d1
130.132.0.0/24
130.132.2.0/24
130.132.3.0/24
intradomain routing uses /24
130.132.1.0/24
Notes: Does not have to be 24; some can be, say 22.