## Slide 1: Network Layer: Link Layer; Course Summary
Qiao Xiang, Congming Gao, Qiang Su
  https://sngroup.org.cn/courses/cnns-xmuf25/index.shtml
12/4/2025
This deck of slides are heavily based on CPSC 433/533 at Yale University, by courtesy of Dr. Y. Richard Yang.

## Slide 2: Recap: IP Addressing Scheme: Requirements
Uniqueness: We need an address to uniquely identify each destination
Aggregability : Routing scalability needs flexibility in aggregation of destination addresses
  we want to aggregate as a large set of destinations as possible in BGP announcements
Current: the unit of routing in the Internet is a classless interdomain routing (CIDR) address

## Slide 3
Recap: Network Forwarding: Putting it Together
Forwarding is also called the fast path (upon receiving each packet)
Slow path: not per packet
  Get IP address (DHCP, or static)
  Setup/compute routing table

## Slide 4: Recap: Putting it Together: Example 2 (Different Networks): A-> E
Setting: Host A network layer receives a packet above.
Action:
  Host A looks up destination in routing table
    Find next hop should be 223.1.1.4
  Hand datagram to link layer to send inside a link-layer frame
misc
fields
223.1.1.1
223.1.2.3
data
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.3
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
A
B
E
Dest. Net. next router Nhops
223.1.1/24 1
223.1.2/24 223.1.1.4 2
223.1.3/24 223.1.1.4 2
forwarding table in A
0.0.0.0/0 223.1.1.4 -
223.1.4.1
To Internet
C’s MAC
addr
A’s MAC
addr
A’s IP
addr
E’s IP
addr
IP payload
datagram
frame
frame dst, src addr
datagram source,
dest address
C

## Slide 5: Recap: Look Inside a Router: Output Port
Buffering required when datagrams arrive from fabric faster than the transmission rate
Queueing (delay) and loss due to output port buffer overflow !
Scheduling and queue/buffer management choose among queued datagrams for transmission

## Slide 6: Recap: Putting it Together: Example 2 (Different Networks): A-> E
misc
fields
223.1.1.1
223.1.2.3
data
Dest. Net router Nhops interface
223.1.1/24 - 1 223.1.1.4
223.1.2/24 - 1 223.1.2.9
223.1.3/24 - 1 223.1.3.27
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.3
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
A
B
E
forwarding table in router
0.0.0.0/0 - - 223.1.4.1
223.1.4.1
To Internet
Setting: Packet above arrives at Router C’s network layer.
Action:
  Router C conducts standard router actions
    Assume packet correct, find next hop should be 223.1.2.9
  Hand datagram to link layer to send inside a link-layer frame
C
E’s MAC
addr
C’s MAC
addr
A’s IP
addr
E’s IP
addr
IP payload
datagram
frame
frame dst, src addr
datagram source,
dest address
datagram arrives at 223.1.2.3!! (hooray!)

## Slide 7
Outline
Admin and recap
Network layer
Link layer
  Overview
  Media access
  Link layer forwarding

## Slide 8
Multiple Access Links and Protocols
Many link layers use broadcast (shared wire or medium)
  traditional Ethernet; Cable networks
  802.11 wireless LAN; cellular networks
  satellite
Problem: if two or more simultaneous transmissions, due to interference, only one node can send successfully at a time (see CDMA later for an exception)

## Slide 9
Multiple Access Protocol
Protocol that determines how nodes share channel, i.e., determines when nodes can transmit
Communication about channel sharing must use channel itself !
Discussion: properties of an ideal multiple access protocol.

## Slide 10
Ideal Mulitple Access Protocol
Broadcast channel of rate R bps
Efficiency: when only one node wants to transmit, it can send at full rate R
Rate allocation:
  simple fairness: when N nodes want to transmit, each can send at average rate R/N
  we may need more complex rate control
Decentralized:
  no special node to coordinate transmissions
  no synchronization of clocks
Simple

## Slide 11
MAC Protocols
Goals
efficient, fair, decentralized, simple
Three broad classes:
non-partitioning
  random access
    allow collisions
  “taking-turns”
    a token coordinates shared access to avoid collisions
channel partitioning
  divide channel into smaller “pieces” (time slot, frequency, code)

## Slide 12: Focus: Random Access Protocols
Examples of random access MAC protocols:
  slotted ALOHA and pure ALOHA
  CSMA and CSMA/CD, CSMA/CA
  Ethernet, WiFi 802.11
Key design points:
  when to access channel?
  how to detect collisions?
  how to recover from collisions?

## Slide 13: Slotted Aloha [Norm Abramson]
Time is divided into equal size slots (= pkt trans. time)
Node with new arriving pkt: transmit at beginning of next slot
If collision: retransmit pkt in future slots with probability p, until successful.
Success (S), Collision (C), Empty (E) slots

## Slide 14: Slotted Aloha in Real Life
Notations:
  Broadcast control channel (BCCH): from base station, announces cell identifier, synchronization
  Random access channel (RACH): MSs for initial access, slotted Aloha
  access grant channel (AGCH): BTS informs an MS its allocation
  standalone dedicated control channel (SDCCH): signaling and short message between MS and an MS
  Traffic channels (TCH)
call setup in GSM
BTS
MS
RACH (request signaling channel)
AGCH (assign signaling channel)
SDCCH (request call setup)
SDCCH (assign TCH)
SDCCH message exchange
Communication

## Slide 15: Slotted Aloha Efficiency
Q: What is the fraction of successful slots?
suppose n stations have packets to send
suppose each transmits in a slot with probability p
- prob. of succ. by a specific node: p (1-p)(n-1)
- prob. of succ. by any one of the N nodes
S(p) = n * Prob (only one transmits)
= n p (1-p)(n-1)

## Slide 16: Goodput vs. Offered Load for Slotted Aloha
S = throughput = “goodput”
(success rate)
G = offered load = np
0.5
1.0
1.5
2.0
Slotted Aloha
when p n < 1, as p (or n) increases
  probability of empty slots reduces
  probability of collision is still low, thus goodput increases
when p n > 1, as p (or n) increases,
  probability of empty slots does not reduce much, but
  probability of collision increases, thus goodput decreases
goodput is optimal when p n = 1, n -> infinite, S -> 1/e (~37%)

## Slide 17: Dynamics of (Slotted) Aloha
Slotted Aloha has maximum throughput when np = 1
  Implies we need to adjust p as the number of backlog stations varies.
Early design question: what is the effect if we do not change p-–use a fixed p
  Assume we have a total of m stations (the machines on a LAN):
    n of them are currently backlogged, each tries with a (fixed) probability p
    the remaining m-n stations are not backlogged. They may start to generate packets with a probability pa, where pa is much smaller than p

## Slide 18: Model
n backlogged
each transmits with prob. p
m-n: unbacklogged
each transmits with prob. pa

## Slide 19: Dynamics of Aloha: Effects of Fixed Probability
n: number of backlogged
stations
0
m
successful transmission rate at offered load np + (m-n)pa
new arrival rate: (m-n) pa
desirable stable point
undesirable stable point
Lesson: if we fix p, but n varies, we may have an undesirable stable point
offered load = 1
- assume a total of
m stations
pa << p
success rate is the departure rate, the rate the backlog is reducing
dep.
and
arrival
rate
of
backlogged
stations

## Slide 20
Summary of Problems of Aloha Protocols
Problems
  slotted Aloha has better efficiency than pure Aloha but clock synchronization is hard to achieve
  Aloha protocols have low efficiency due to collision or empty slots
    when offered load is optimal (p = 1/N), the goodput is only about 37%
    when the offered load is not optimal, the goodput is even lower
  undesirable steady state at a fixed transmission rate, when the number of backlogged stations varies
Ethernet design: address the problems:
  optimal transmission rate
Notes: Slotted aloha Implied requirement: clock synchronization
Pure aloha, no sync, but even lower performance, ½ of slotted aloha, in textbook

## Slide 21
The Basic MAC Mechanisms of Ethernet
get a packet from upper layer;
  K := 0; n := 0; // K: control wait time; n: no. of collisions
  repeat:
  wait for K * 512 bit-time;
  while (network busy) wait;
  wait for 96 bit-time after detecting no signal;
  transmit and detect collision;
  if detect collision
  stop and transmit a 48-bit jam signal;
  n ++;
  m:= min(n, 10), where n is the number of collisions
  choose K randomly from {0, 1, 2, …, 2m-1}.
  if n < 16 goto repeat
  else give up

## Slide 22: Ethernet
“Dominant” LAN technology:
First widely used LAN technology
Kept up with speed race: 10 Mbps, 100 Mbps, 1 Gbps, 10 Gbps
Metcalfe’s Ethernet
sketch

## Slide 23
Outline
Admin and recap
Link layer
  Ethernet switch

## Slide 24: Ethernet Switch
link-layer device: takes an active role
  store, forward Ethernet frames
  examine incoming frame’s MAC address, selectively forward frame to one-or-more outgoing links when frame is to be forwarded on segment, uses CSMA/CD to access segment
transparent
  hosts are unaware of presence of switches
plug-and-play, self-learning
  switches do not need to be configured

## Slide 25: Switch: Multiple Simultaneous Transmissions
hosts have dedicated, direct connection to switch
switches buffer packets
Ethernet protocol used on each incoming link, but no collisions; full duplex
  each link is its own collision domain
switching: A-to-A’ and B-to-B’ can transmit simultaneously, without collisions
switch with six interfaces
(1,2,3,4,5,6)
A
A’
B
B’
C
C’
1
2
3
4
5
6

## Slide 26: Switch Forwarding Table
Q: how does switch know A’ reachable via interface 4, B’ reachable via interface 5?
switch with six interfaces
(1,2,3,4,5,6)
A
A’
B
B’
C
C’
1
2
3
4
5
6
A: each switch has a switch table, each entry:
  (MAC address of host, interface to reach host, time stamp)
  looks like a routing table!
Q: how are entries created, maintained in switch table?
  something like a routing protocol?

## Slide 27: Switch: Self-Learning
A
A’
B
B’
C
C’
1
2
3
4
5
6
switch learns which hosts can be reached through which interfaces
  when frame received, switch “learns” location of sender: incoming LAN segment
  records sender/location pair in switch table
A A’
Source: A
Dest: A’
MAC addr interface TTL
Switch table
(initially empty)
A
1
60

## Slide 28: Switch: Frame Filtering /Forwarding
when frame received at switch:
  1. record incoming link, MAC address of sending host
  2. index switch table using MAC destination address
  3. if entry found for destination then {
  if destination on segment from which frame arrived then drop frame
  else forward frame on interface indicated by entry
  }
  else flood /* forward on all interfaces except arriving
  interface */

## Slide 29: Self-Learning, Forwarding: Example
A
A’
B
B’
C
C’
1
2
3
4
5
6
A A’
Source: A
Dest: A’
MAC addr interface TTL
switch table
(initially empty)
A
1
60
A A’
A A’
A A’
A A’
A A’
frame destination, A’, location unknown:
flood
A’ A
destination A location known:
A’
4
60
selectively send
on just one link

## Slide 30: Interconnecting Switches
self-learning switches can be connected together:
Q: sending from A to G - how does S1 know to forward frame destined to G via S4 and S3?
A: self learning! (works exactly the same as in single-switch case!)
A
B
S1
C
D
E
F
S2
S4
S3
H
I
G
Notes: Network needs to be a tree

## Slide 31: Self-Learning Multi-switch Example
Suppose C sends frame to I, I responds to C
Offline Exercise: show switch tables and packet forwarding in S1, S2, S3, S4
A
B
S1
C
D
E
F
S2
S4
S3
H
I
G

## Slide 32: Institutional Network
to external
network
router
IP subnet
mail server
web server

## Slide 33: Switches vs. Routers
both are store-and-forward:
routers: network-layer devices (examine network-layer headers)
switches: link-layer devices (examine link-layer headers)
both have forwarding tables:
routers: compute tables using routing algorithms, IP addresses
switches: learn forwarding table using flooding, learning, MAC addresses
application
transport
network
link
physical
network
link
physical
link
physical
switch
datagram
application
transport
network
link
physical
frame
frame
frame
datagram

## Slide 34
Outline
Course Summary

## Slide 35: Synthesis: A Day in the Life of a Web Request
journey down protocol stack complete!
  application, transport, network, link
putting-it-all-together: synthesis!
  goal: identify, review, understand protocols (at all layers) involved in seemingly simple scenario: requesting www page
  scenario: student attaches laptop to campus network, requests/receives www.tencent.com

## Slide 36: A Day in the Life: Scenario
Comcast network
68.80.0.0/13
Tencent’s network
64.233.160.0/19
64.233.169.105
web server
DNS server
school network
68.80.2.0/24
web page
browser

## Slide 37: A Day in the Life… Connecting to the Internet
router
(runs DHCP)
connecting laptop needs to get its own IP address, addr of first-hop router, addr of DNS server: use DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP request encapsulated in UDP, encapsulated in IP, encapsulated in 802.3 Ethernet
Ethernet frame broadcast (dest: FFFFFFFFFFFF) on LAN, received at router running DHCP server
Ethernet demuxed to IP demuxed, UDP demuxed to DHCP

## Slide 38: A Day in the Life… Connecting to the Internet
router
(runs DHCP)
DHCP server formulates DHCP ACK containing client’s IP address, IP address of first-hop router for client, name & IP address of DNS server
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
encapsulation at DHCP server, frame forwarded (switch learning) through LAN, demultiplexing at client
Client now has IP address, knows name & addr of DNS
server, IP address of its first-hop router
DHCP client receives DHCP ACK reply

## Slide 39: A Day in the life… ARP (before DNS, before HTTP)
router
(runs DHCP)
before sending HTTP request, need IP address of www.tencent.com: DNS
DNS
UDP
IP
Eth
Phy
DNS
DNS
DNS
DNS query created, encapsulated in UDP, encapsulated in IP, encapsulated in Eth. To send frame to router, need MAC address of router interface: ARP
ARP query broadcast, received by router, which replies with ARP reply giving MAC address of router interface
client now knows MAC address of first hop router, so can now send frame containing DNS query
ARP query
Eth
Phy
ARP
ARP
ARP reply

## Slide 40: A Day in the Life… Using DNS
router
(runs DHCP)
DNS
UDP
IP
Eth
Phy
DNS
DNS
DNS
DNS
DNS
IP datagram containing DNS query forwarded via LAN switch from client to 1st hop router
IP datagram forwarded from campus network into Comcast network, routed (tables created by RIP, OSPF, IS-IS and/or BGP routing protocols) to DNS server
demuxed to DNS server
DNS server replies to client with IP address of www.tencent.com
Comcast network
68.80.0.0/13
DNS server
DNS
UDP
IP
Eth
Phy
DNS
DNS
DNS
DNS

## Slide 41: A Day in the Life…TCP Connection Carrying HTTP
router
(runs DHCP)
HTTP
TCP
IP
Eth
Phy
HTTP
to send HTTP request, client first opens TCP socket to web server
TCP SYN segment (step 1 in 3-way handshake) inter-domain routed to web server
TCP connection established!
64.233.169.105
web server
SYN
SYN
SYN
SYN
TCP
IP
Eth
Phy
SYN
SYN
SYN
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
web server responds with TCP SYNACK (step 2 in 3-way handshake)

## Slide 42: A Day in the Life… HTTP Request/Reply
router
(runs DHCP)
HTTP
TCP
IP
Eth
Phy
HTTP
HTTP request sent into TCP socket
IP datagram containing HTTP request routed to www.tencent.com
IP datagram containing HTTP reply routed back to client
64.233.169.105
web server
HTTP
TCP
IP
Eth
Phy
web server responds with HTTP reply (containing web page)
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
web page finally (!!!) displayed

## Slide 43: Course Topics Summary
The Internet is a general-purpose, large-scale, distributed computer network
Major design features/principles
  packet switching/statistical multiplexing
    time-reversibility, queueing theory and performance analysis
  layered architecture, hour-glass architecture
    end-to-end principle
  decentralized (social-technocal) architecture
    e.g., DNS (hierarchy delegation), interdomain routing (peer-to-peer)
  resource allocation framework
    axiom-based design (NBS); optimization decomposition through duality
  adaptive control
    e.g., sliding window self clocking, AIMD adaptation, Ethernet exp backoff
  tradeoff between theoretical impossibility and practice

## Slide 44: First-Day Class: What is a Network Protocol?
A network protocol defines the format and the order of messages exchanged between two or more communicating entities, as well as the actions taken on the transmission and/or receipt of a message or other events.
Protocols that we have touched on?

## Slide 45: First-Day Class: Internet Physical Infrastructure
Backbone ISP
ISP
ISP
Campus access, e.g.,
  Ethernet
  Wireless
The Internet is a network of networks
Each individually administrated network is called an Autonomous System (AS)
https://www.google.com/loon/how/
data center
Residential access
  Cable, Fiber, DSL, Wireless

## Slide 46: First-Day Class: General Complexity
Complexity in highly organized systems arises primarily from design strategies intended to create robustness to uncertainty in their environments and component parts.
  Scalability is robustness to changes to the size and complexity of a system as a whole.
  Evolvability is robustness of lineages to large changes on various (usually long) time scales.
  Reliability is robustness to component failures.
  Efficiency is robustness to resource scarcity.
  Modularity is robustness to component rearrangements.
David Meyer

## Slide 47: First-Day Class: Evolution
Driven by Technology, Infrastructure, Policy, Applications (usage), and Understanding:
  technology
    e.g., wireless/optical communication technologies and device miniaturization (sensors)
  infrastructure
    e.g., cloud computing vs local computing
  applications (usage)
    e.g., mobile computing, content distribution, game, tele presence, sensing
  understanding
    e.g., resource sharing principle, routing principles, mechanism design, optimal stochastic control (randomized access)
Complexity comes from evolution.
Don’t be afraid to challenge the foundation and redesign!